ROUTINE

R 150124Z DEC 98 PSN 057348I27

FM COMNAVSURFPAC SAN DIEGO CA//N434//

TO NAVSURFPAC AFLOAT

INFO CINCPACFLT PEARL HARBOR HI//N43//

PEO TAD SC WASHINGTON DC//PMS400F//

PEO EXW WASHINGTON DC//307/312//

COMNAVAIRPAC SAN DIEGO CA//N43//

COMNAVSURFLANT NORFOLK VA//N43//

COMNAVSEASYSCOM WASHINGTON DC//03Z/03Z62/91//

NAVSURFWARCEN SHIPSYSENGSTA PHILADELPHIA PA//9342//

INSURVPAC SAN DIEGO CA//00//

COMNAVSAFECEN NORFOLK VA//34//

FLETRACEN SAN DIEGO CA//N33//

SERVSCOLCOM GREAT LAKES IL//20//

COMAFLOATRAGRUPAC SAN DIEGO CA//JJJ//

UNCLAS//N09302//

MSGID/GENADMIN/COMNAVSURFPAC//

SUBJ/GUIDANCE FOR PLUGGING OF MEGGER HOLES ON ELECTRICAL POWER

/DISTRIBUTION PANELS//

REF/A/GENADMIN/NAVSEA/230319ZNOV98/-/NOTAL//

POC/GRANDONA/LT/N4343/TEL:619 437-2500/TEL:DSN 577-2500//

RMKS/1.  BACKGROUND. SAFETY CONCERNS WITH ELECTRICAL POWER

DISTRIBUTION PANEL MEGGER HOLES WAS FIRST ADDRESSED DURING INSURV

AND OTHER SAFETY RELATED INSPECTIONS.  PART OF THE ORIGINAL CONCERN

WAS HOW THE MEGGER HOLES WERE BEING COVERED.  BASED ON INSPECTION

FINDINGS, SOME SHIPS WERE NOT COVERING SUBJ MEGGER HOLES, OTHERS

WERE COVERING HOLES BY VARIOUS MEANS AND MATERIALS.  IN SOME

CASES EFFORTS PROVED TO BE MORE OF A HAZARD BECAUSE OF FIRE

POTENTIAL. CLARIFICATION FOR TREATMENT OF MEGGER

HOLES WAS REQUESTED JUN 96 TIME FRAME.  NAVSEA ISSUED INITIAL MSG

GUIDANCE AUG 96.  NAVSEA RECOMMENDED PLUGGING OF MEGGER HOLES WITH

NYLON NON-TOXIC PLUGS, HEYCO MOLDED PRODUCTS (P/N 2616).  THESE

PLUGS WERE NOT AVAILABLE IN NAVY SUPPLY SYSTEM.  REF A, QUOTED

BELOW, IS NAVSEA REVISED RECOMMENDATION FOR PLUGGING OF ELECTRICAL

POWER DISTRIBUTION PANEL MEGGER HOLES.

2.  BASED ON REVIEW OF ORIGINAL CONCERNS, ALL CNSP SHIPS ARE DIRECTED

TO REMOVE OTHER MEANS USED TO COVER/PLUG ELECTRICAL POWER

DISTRIBUTION PANEL MEGGER HOLES AND INSTALL PLUGS

(NSN 5340-01-081-1718) IDENTIFIED REF A.  ALL MEGGER HOLES ON

ELECTRICAL POWER PANELS SHOULD BE PLUGGED USING MATERIAL IDENTIFIED

PARA 1 OF REF A BY 31 JUN 99.

QUOTE

R 230319Z NOV 98 ZYB

FM COMNAVSEASYSCOM WASHINGTON DC/03Z/

TO COMNAVSURFPAC SAN DIEGO CA/N431/N4311/

COMNAVSURFLANT NORFOLK VA/N43/

COMNAVAIRPAC SAN DIEGO CA/N43/

COMNAVAIRLANT NORFOLK VA/N43/

COMNAVSAFECEN NORFOLK VA/34/30/312/

COMREGSUPPGRU MAYPORT FL/N82/

CINCLANTFLT NORFOLK VA/N43/

CINCPACFLT PEARL HARBOR HI/N43/

PRESINSURV NORFOLK VA/00/

INSURVPAC SAN DIEGO CA/01/

COMAFLOATRAGRULANT NORFOLK VA/N43/

NAVSURFWARCEN SHIPSYSENGSTA PHILADELPHIA PA/01/

LANTFLT PEB NORFOLK VA/N74/

PACFLT PEB SAN DIEGO CA/N1/

FTSCLANT NORFOLK VA/4211/

FTSCPAC SAN DIEGO CA/91/

INFO COMNAVSEASYSCOM WASHINGTON DC/03Z45/

UNCLAS  /N09330/

MSGID/GENADMIN/NAVSEA 03Z45/

SUBJ/GUIDANCE FOR ELECTRICAL POWER DISTRIBUTION PANELS/

REF/A/GENADMIN/COMNAVSEASYSCOM/280317ZAUG96/

NARR/REF A PROVIDED GUIDANCE FOR PLUGGING POWER PANEL MEGGER

HOLES./

RMKS/1.  REF A RECOMMENDED THAT ALL POWER PANEL MEGGER HOLES

BE COVERED BECAUSE OF SAFETY CONCERNS AND THE FACT THAT THERE

IS NO REQUIREMENT TO USE THE HOLES.  REF A RECOMMENDED THAT

THE FLEET USE A PLUG MANUFACTURED BY HEYCO MOLDED PRODUCTS

(P/N 2616).  HOWEVER, THIS PLUG WAS NOT PROCURED AND A STOCK

NUMBER WAS NEVER ASSIGNED TO IT.  CNSL RECENTLY INFORMED

NAVSEA THAT A DIFFERENT PLUG THAT FITS THE MEGGER HOLE IS ALREADY

SUPPORTED BY THE STOCK SYSTEM.  NAVSEA RECOMMENDS THAT THE MEGGER

HOLES BE COVERED USING NSN 5340-01-081-1718.

2.  THE TPOC IS MR. GEORGE RASICH, SEA 03Z45, DSN 332-5340

OR COMM (703) 602-5340 X393.//

UNQUOTE

BT

NNNN

RTD:000-000/COPIES: