ROUTINE

R 041430Z FEB 00

FM COMNAVSAFECEN NORFOLK VA//30B/FILE//

TO AIG 6942

AIG 6943

UNCLAS //N05100//

MSGID/GENADMIN/COMNAVSAFECEN/34-035/FEB//

SUBJ/ COMNAVSAFECEN AFLOAT SAFETY ADVISORY 3-00, DUMBWAITER

AND CONVEYOR INSPECTION CRITERIA//

REF/A/DOC/COMNAVSEASYSCOM/10DEC98//

REF/B/GENADMIN/COMNAVSAFECEN/101334ZJAN00//

NARR/REF A IS ACN TO NSTM 572, SHIPBOARD STORES AND

PROVISIONS HANDLING (LETTER 9780 SER 03P8/029).  REF B IS

AFLOAT SAFETY ADVISORY 2-00.//

POC/S. V. SCUDDER/GS12/DSN: 564-3520/X7115-/NAVSAFECEN

30B/(757)444-3520/X7115/E-MAIL:

SSCUDDER(AT)SAFETYCENTER.NAVY.MIL (ALL LOWER CASE)/

RMKS/1.  REF A PROVIDES MACHINERY FEATURES AND IN-SERVICE

LIMITS FOR DUMBWAITERS AND CONVEYORS.  IT IS A VALUABLE TOOL

WHEN PREPARING FOR INSPECTIONS, ASSIST VISITS, AND WHEN

CHECKING THE SAFETY FEATURES DURING PMS.

2.  DURING OUR REVIEW OF REF A, WE FOUND THAT THE ACN WAS

NOT SENT DIRECTLY TO SHIPS.  WE RECOMMEND YOU REVIEW YOUR

FILES TO SEE IF YOU HOLD REF A.  IF NOT, CONTACT YOUR CHAIN

OF COMMAND.

3.  REF B IS THE LAST ADVISORY WE SENT TO AIG'S 6942 AND

6943: AUTO-INFLATABLE LIFE PRESERVERS MK-1 AND AUTO-

INFLATABLE UTILITY LIFE PRESERVER MK-5 MOD 0.//

BT

NNNN

NAVAL SEA SYSTEMS COMMAND

2531 JEFFERSON DAVIS HWY

ARLINGTON VA 22242-5105

9780

Ser 03P8/029

10 DEC 1998

From:	Commander, Naval Sea Systems Command

To:		Distribution

Subj:	ADVANCED CHANGE NOTICE TO NAVAL SHIPS TECHNICAL MANUAL

S9086-TL-STM-010, CHAPTER 572, SHIPBOARD STORES AND PROVISIONS HANDLING

Ref:	    (a) Naval Ships Technical Manual, COMNAVSEASYSCOM

S9086-TL-STH-010N Chapter 572

Encl:	(1) S9086-TL-STM-010/CH-572, Dumbwaiter Feature

In-Service Limits

(2) S9086-TL-STM-010/CH-572, Conveyor Feature In-Service

Limits

(3) Conveyor Component Load Test Requirement

1.	This is an Advance Change Notice (ACN) to reference (a) which is currently undergoing a major revision.  The changes promulgated by this ACN will be incorporated into that revision.  Record entry of this ACN on the "Record of Change" in the front of reference (a).

2.	Enclosures (1) through (3) provided by this ACN are intended for immediate use for all Dumbwaiter and Conveyor inspections.

3. The technical point of contact is Mr. M. Royle, COMNAVSEASYSCOM 03P8, commercial (703) 602-1846 x203.

K. P. ROEY

By direction

Distribution:

CINCLANTFLT (N43)

CINCPACFLT (N43)

COMNAVAIRLANT (N43)

COMNAVSURFLANT (N43)

COMNAVSUBLANT (N43)

COMNAVAIRPAC (N43)

COMNAVSURFPAC (N43)

COMNAVSUBPAC (N43)

NSWC PHD (4MOO)

NSWCCD-SSES

PRESINSURV

FTSCLANT (432)

FTSCFAC (306)

Some or all of the following features may be installed on a dumbwaiter.  If installed, the following criteria is applicable:

FEATURES	IN-SERVICE LIMITS

MACHINERY

1.	Machinery foundations, welds 	All fasteners are properly sized, installed and tight.

and fasteners	No cracked, deformed, loose or missing components

apparent by visual and hands-on inspection.  No

more than 15% loss in material thickness or strength

bearing portions permitted.

2.	Brake	Platform with rated load shall stop at and maintain

deck level.  Brake adjustments shall meet the

requirements in the applicable MRC.  No loose

electrical connections based on visual inspection.  No

loose or missing fasteners, which would result in

brake failure.

3.	Reduction Sears	No unusual noise during operation.

4.	Hoisting machinery shafts/	All fasteners are properly sized, installed and tight.

couplings/bearings/keys/	No cracked, deformed or missing components

keyways	apparent by visual and hands-on inspection.  No

unusual noise during operation.

5.		Hoist wire rope sheaves	Sheaves shall rotate freely and have no unusual noise

during operation. Sheave foundations and ship

structure at foundations are free of visual cracks or deformation.

All fasteners are properly sized installed and tight.

6.	Hoist wire ropes	No kinks visible with wire rope tensioned

by weight of platform.  No visible signs of “hour

glass” shaped wire ropes indicating failed core.  No

more than 6 broken wires per rope lay length or no

more than 3 broken wires per strand in a rope lay

length.

7.	Hoist wire rope and fittings	No cracked, deformed, loose or missing components

apparent by visual and hand-on inspection. No

evidence of wire rope pulling from end fitting.  Fiege

fittings shall have wires visible through the

inspection hole.

Enclosure (1) Sheet 1 of 5

8.	Hoist rope end fitting-to- 	All fasteners/hardware are property sized. installed

platform or trunk attachments	and tight.  No cracked. deformed. loose or missing

components apparent by visual and hands-on

inspection.  No more than 15% loss in material

thickness of strength bearing portions is permitted.

9.	Platform structure	No cracked. deformed, loose or missing components

apparent by visual and hands-on inspection, No

more than 15% loss in material thickness of

strength bearing portions is permitted.

10.	Guide roller/blocks/	Guide rollers/blocks/gibes and shoes shall be

guide plates/ shoes	adjusted to prevent the platform from shifting more

than +/- 3/8 inch in the horizontal direction when

loading the platform.  No cracked, deformed, loose

or missing components apparent by visual and

hands-on inspection.  All fasteners are properly sized,

installed, and tight.

11.	Guide rails		No cracked, deformed, loose or missing components

apparent by visual and hands-on inspection.  All

fasteners are properly sized, installed, and tight.

Some or all of the following features may be installed on a dumbwaiter.  If installed, the following criteria is applicable:

SAFETY DEVICES

1.	Overspeed governors (0SG)	When the 0SG is actuated the OSG shall engage the

Mechanical Safety Subsystem (MSS) stopping the

platform.

When the OSG is actuated, OSG switch shall remove

power to the hoist motor and brake causing the. brake

to set, OSG counterweights shall move freely

throughout the full range of motion and contact the

OSG stop (bail) block. No cracked, deformed, loose,

or missing components apparent by visual and

hands-on inspection.

The OSG shall have been calibrated within the last

six years and the trip speed adjustment shall be

locked-wired or sealed to provide an indication if the

adjustment was changed.

2.	Broken rope safety device 	Slacking of the hoist rope shall cause the BRSD

(BRSD)	to engage the MSS.

Enclosure (1) Sheet 2 of 5

3.	Mechanical Safety Subsystem	When the OSG is actuated with the platform moving

downward in free fall (after the platform has

traveled less than one deck height while manually

releasing the brake) the MSS shall set the safety

devices, (wedges, knurled rollers, eccentric cams),

stopping the platform.

When the BRSD is actuated. the MSS shall set as

stated above.

4.	Spring-buffers in pit	No cracked or deformed components apparent by

visual and hands-on inspection.  All springs are in

place and free to compress. The springs, foundation

and supporting deck shall have no more than 15%

loss in material thickness.

5.	Hoist Wire Pope Slack Rope	When actuated (platform resting on buffer springs,

Device	rope slack) the slack rope device shall disconnect

power to the hoist motor causing the brake to set.

6.	Personnel guards around	Guards shall be installed around all wire rope drums,

rotating machinery	exposed gears, and hoist wire ropes that are easily

accessible to operating personnel.

7.	Door interlocks	Each door (platform or trunk) shall be interlocked

with the control system so that all doors must be

closed before the platform can be jogged dispatched

or called.

Mechanical interlocks shall prevent opening unless

the platform is at a deck level.

Some or all of the following features may be installed on A dumbwaiter. If installed, the following criteria is applicable:

CONTROLS

1.	Dumbwaiter controllers	Dumbwaiter successfully dispatches and stops

at each level.  Dumbwaiter does not exhibit

inadvertent starts, stops or unexpected response to

control switches.  No moisture or broken connections

apparent in the controller based on visual inspection.

2.	Platform mounted targets	Targets (vanes/flags/cams) shall be correctly oriented

(Vanes/flags/cams) to	and securely actuate trunk switches mounted to the

platform. no cracked, deformed. loose or missing

components apparent by visual and hands-on

inspection.

Enclosure (1) Sheet 3 of 5

3.	In-trunk platform control 	Switches are correctly oriented and securely fastened.

switches	Platform slow stop. and over travel switches shall

function as intended when actuated by

platform mounted target (vanes/flags/cams).

Proximity switches shall have at least 1/2 of the switch

face covered by the platform mounted target

(vanes/flags/cams).  Targets (vanes/flags/cams) shall

be oriented so that sufficient clearance between the

switch and the cam is established to effectively allow

switch actuation.

Mechanical limit switch actuating arm shall be

aligned to strike the center of the platform-mounted

target (vane, flags/cams).

Capture (vane) type switches shall be aligned with

the switch vane such that the switch body and vane

do not come in contact with each other throughout

the full travel of the vane through the switch.

4.	Run/Stop switches	When placed in the STOP position shall prevent

dumbwaiter operation.

5.	Safety Switch	When opened shall secure power to the

dumbwaiter.

6.	Emergency Stop	When actuated shall prevent dumbwaiter operation

by opening the control power circuit.

If equipped with a Shunt trip or Undervoltage safety

circuit, depressing of an Emergency Stop switch shall

disconnect circuit power to the dumbwaiter.

Some or all of the following features may be installed on a dumbwaiter. If installed, the following criteria is applicable:

CLOSURES

1.	Closure hinges	Hinges and their attachments to ship’s structure

shall not have any missing, loose or damage

hardware or visible cracks.  Hinges shall operate

freely through entire range of motion without

unusual noise.

Enclosure (1) Sheet 4 of 5

,

2.	Door guides and rails/rollers	Door rollers shall be securely attached and

sufficiently engage the guides or rails to avoid door

coming adrift.  Doors shall operate freely through the

complete range of motion. No cracked, loose or

missing components apparent by visual and

hand-on inspection.

3.	Door wire ropes and end	No kinks visible with wire rope under normal

fittings	tension.  No more than 6 broken wires per rope by

length or no more than 3 broken wires per strand in a

rope lay length.

No cracked, deformed, loose or missing components

apparent by visual and hands-on inspection of the

end fittings.  No evidence of the wire rope pulling

from and fitting.  Fiege fittings shall have wires

visible through the inspection hole.

Enclosure (1) Sheet 5 of 5

This is the list of features which must be in good working condition for a conveyor to be considered safe to operate.  It also provides the in-service limits for the material condition of each feature.

The in-service limits arc to be used during normal conveyor operation, troubleshooting, scheduled maintenance, and as the basis for other inspections such as conveyor support unit visits and underway material inspections.  When any of the applicable listed features has deteriorated beyond these limits, the conveyor is unsafe to operate.  The deteriorated feature must be repaired, readjusted or replaced prior to further conveyor operation.  When deteriorated feature(s) cannot be repaired or replaced in a timely manner, and mission essential conveyor operation is being suspended, a request for Departure From Specification (DFS) shall be submitted.  The DFS will be approved only when operational restrictions or alternative means of attaining conveyor safety can be implemented.  COMNAVSEASYSCOM provides recommended operating restrictions and/or other guidance to mitigate potential safety hazards where features listed in Appendix C were not originally installed

The following Note is provided to clarify “securely fastened” as used throughout Appendix C (In-Service Limits):

NOTE:  In-Service Limits referring to this note include component parts such as:  keys, collars, caps, fasteners, setscrews, and all other such parts that may work loose.  Keys, collars, etc. shall be fastened securely by use of setscrew(s) or other suitable method that will mitigate the component from working loose.  Threaded parts, connecting link pins, etc. shall be fastened securely by use of cotter pins, safety wire or other suitable method that will mitigate the component from working loose.

Enclosure (2) Sheet 1 of 11

1.	FEATURES	IN-SERVICE LIMITS

MACHINERY

Machinery foundations,	All fasteners are securely fastened (see note), proper

welds, and fasteners 	size and type, installed and tightened.  No cracked,

deformed, loose or missing components apparent

by visual and hands-on Inspection. No more than 15%

loss in material thickness of strength bearing

portions is permitted,

2.	Brake	Unloaded conveyor stops in either up or down

direction without any visible drift noted. Brake

adjustment shall meet the requirement of the

applicable MRC.  No loose electrical connections

based on visible inspection.  No loose or miming

fasteners which would directly result in brake failure.

No damaged or missing manual release handle.

3.	Reduction gear	No unusual noise during operation. Oil is at proper level. Breather cap is installed without defect.

4.	Torque limiter coupling	No conveyor slippage visible during start-up or

normal operation, in either up or down direction.

with no -load or working load. Chain not broken or

missing.

5.	Hoisting machinery	All fasteners are securely fastened (see note), proper

shaft/couplings/bearings/	size and type, installed and tightened.  No cracked,

keys/keyways/pillow -	deformed, worn, loose, or missing components

blocks/fasteners 	apparent by visual and hands-on inspection,

6.	Drive/driven/carrier	All fasteners are securely fastened (see note), proper

sprockets	size, installed and tight.  Sprockets shall rotate freely

and have no unusual noise during operation.  No

uneven wear, broken or cracked teeth apparent by

visual and hands-on inspection.  Sprockets are

properly aligned and parallel (as appropriate) to each

other.

7.	Head and tail cam track	All fasteners are securely fastened (see note), proper

assemblies	size and type, installed, and tightened.  No bent,

flared, deformed or unusual wear to cam tracks

apparent by visual inspection.  No cam track to cam

plate weldment cracks or deformation apparent by

visual inspection.

Enclosure (2) Sheet 2 of 11

No binding or banging of carrier tray assembly motion through transition from horizontal to vertical position and return, apparent during operation or apparent by visual inspection of tracks.  Head and tail cam plate assembly cam tracks to intermediate cam tracks have no more than a ¼ inch gap, and are in alignment to each other apparent by visual and hands an measurements.  Tail cam plate adjusting rod, spring, and adjusting and jam (locking) nuts are proper size and type, installed and tightened without any unusual wear apparent by visual and hands-on inspection.  Adjustment assembly is not at its maximum, and to loose, or minimum, and to right, limits.

8.	Drive and carrier chains	No corroded, deformed, worn, loose, broken or

missing rollers, bent or cracked side plates, and

loose, worn, deformed, improperly or not installed

link pins apparent by visual and hands-on inspection.

No lag between drive and driven sprockets during

start-up and stopping, and no-bounce or drift of the

carrier trays during stopping apparent by visual

inspection.  Adjust chain tension in accordance with

applicable MRC.

9.	Carrier trays, mounting	All fasteners arm securely fastened (see note), proper

blocks, guide arms,	size and type, installed and tightened.  No. deformed

spacers, guide rollers,	carrier trays, tray tines, no missing or deformed guide

fasteners	arms, mounting block or shafts, no sheared, damaged

fasteners or missing guide arm rollers, and missing spacers.

10.	Conveyor. trunk	All fasteners are securely fastened (see note), proper

foundation, welds, bracing	size and type, installed and tightened. No bent,

(4 point). and fasteners	loose, or missing bracing (4 point) by visual

inspection,  No more than 15% loss in material

thickness of strength bearing portions is permitted.

No cracks, corrosion or deformation of welds

apparent by visual and hands-on inspection.

11.	Intermediate cam tracks	All fasteners are securely fastened (see note), proper

(guide rails).	size and type, installed and tightened. No bent,

flared. deformed, separations (gaps) or unusual wear

to cam tracks apparent by visual inspection.

Intermediate cam tracks to head/tail cam tracks have

no more than a 1/4 inch separation (gap), and are in

alignment to each other apparent by visual and hands

on measurements. Provide for smooth vertical

Enclosure (2) Sheet 3 of 11

movement, of the carrier tray assemblies, in both the vertical and horizontal positions during operation.  Unloaded carrier tray assembly guide rollers shall be free to roll without loading (binding) against cam track throughout the trunk.

12.	Machinery and trunk 	All fasteners are securely fastened (see note), proper

shields and guards	size and type, installed and tightened.  No missing,

bent, flared, deformed, or unusual wear (contact)

from rotating components apparent by visual and

hands-on inspection.

SAFETY DEVICES

13.	Down overtravel assembly	All fasteners are securely fastened (see note), proper

size and type, installed and tightened. No missing, or

deformed platform tray or tray tines. No binding or

sticking of platform felt during hands-on actuation

and platform automatically returns to unactuated

position. Platform tines are horizontal in the unactuated

position. No more than 10-degree rotation of the

switch actuator arm required to actuate the limit switch

apparent by hands-on measurements. A minimum of

15 pounds of pressure will rotate the platform and

actuate the switch

14.	Jam limit assembly	All fasteners securely fastened (see note), proper

size and type, installed, and tightened.  No binding or

sticking of counter weight or tension cable felt during

hands-on actuation.  The tension cable or

photoelectric beam (DD963 Class only) shall  be

located 1 Inch from and parallel to the carrier tray

tine tips apparent by hands-on measurements.  No

more than a 1.5-inch displacement of tension cable

required to actuate the switch apparent by hands-on

measurements.  The switch arm roller shall be 1/32 of

an inch from the top of the counter weight apparent

by hands-on measurements.

15.	Intermediate level	All fasteners am securely fastened (see note), proper

Load/unload assemblies	size and type, installed and tightened.  No deformed

load/unload trays or tray tines, or sheared, damaged

missing load/unload/stow position securing pins.  No

missing, damaged, corroded or misaligned stow

position locking pins and holes.  No greater than ¼

inch side to side slop between mounting brackets

apparent by hands-on, side to side, movement of tray

in the load (horizontal) position, and tray actuates the

down interlock limit switch without fall.  No binding,

Enclosure (2) Sheet 4 of 11

sticking of tray felt during hands-on rotation between positions. Not less than 28 inches or more than 34 inches from top of tray (load position) to deck.

16.	Adjustable Index	Tray will rotate outside of trunk to a position that will

level Load/unload	not interfere with the gravity conveyor.  All other

assemblies		intermediate level load/unload criteria germane.

17.	Fixed, top and	All fasteners are securely fastened (see note), proper

intermediate level, roller,	size and type, installed and tightened.  No missing or

load/unload platform	deformed load/unload platform rollers.

18.	Fixed. top, slide,	All fasteners are securely fastened (see note), proper

load/unload platform	size and type, installed and tightened.  No missing or

deformed load/unload platform tines.  Will be

inclined at not more than a 30-degree angle,

19.	Cleanout door	All fasteners are securely fastened (see note), proper

size and type installed and tightened.  Opening shall

be, at a minimum, 24 inches wide by 16 inches high,

equal to or greater than the tightness of the

contiguous space but not less than water tight,

hinged, and interlocked,

20.	Up overtravel protection	All fasteners are securely fastened.(see note), proper

size and type, installed and tightened.  Shall be of the

photoelectric eye and reflector type and bypassed by

in opened top level door (front “C” or rear “Z” load

station configuration) or by opening either, top level

door on conveyors that have both front and rear load

station doors.  Shall stop conveyor operation by

detecting a 12 by 12 by 6 inch high or larger

package, located anywhere on a carrier tray, from

traveling upward to an  unmanned/unopened top

station level and prevent continued operation’ until’

the package has been removed.  Will not permit any

further upward operation until the detected package

has been removed or down operation without

opening the top level door and only one lower level

door.

21.	Access door		All fasteners are securely fastened, proper size, and

type, installed and tightened.  Opening shall be equal

to or greater than die tightness of the contiguous

space but not less than water tight, hinged, and

interlocked.  No missing or deformed gaskets, hinges

or dogs. Door shall open to at least 90 degree from

Enclosure (2) Sheet 5 of 11

the opening, provide a latching mechanism to hold door in the open position, locking mechanism in the closed position, door block and door control and light interlock switch strikers. Shall not hinder stores movement when opened and latched.

22	Door blocks, mechanical	Not missing, damaged or misaligned.  Will not

permit closing an access door unless the load/unload

device is in the stowed (vertical) position without

fail. Will not pose a personnel safety hazard or hinder

handlers/supervisors from moving packages.  Is

required for all intermediate and bottom level

load/unload stations. Can be replaced by a stow

switch.

23	Top level access hatch	Shall be water right when dogged.  No missing or

deformed gasket, or dogs.  Shall provide hatch

control and light interlock switch strikers.  Shall hot

be removed without safety stanchions and chains

installed.  Gasket shall not take a permanent set.

Trough and drain shall be free of standing water and

debris.  Shall be dogged when installed.

24	Trunk automatic lighting 	All fasteners are securely fastened (see note), proper

fixtures/switch	size and type, installed and tightened.  No missing

damaged, light fixtures or tubes.  Automatically

Illuminate when access hatch/door is opened

Inspect wire for cracked or frayed insulation.

25	Audible warning horn	No missing or defective audible warning horns.  Shall

sound at the sending and. receiving stations being

used for 3 to 3.5 seconds before convey or operation

in either the up or down direction, and stop when

conveyor starts moving.  Shall be the vibratory horn

type with sound level of 85 +/- 3 dB.  Inspect wire

for cracked or frayed insulation.

26	Personnel safety shields	All fasteners are securely fastened (Sec note), proper

size and type, installed and tightened.  Is hinged to

allow for outward swing and have positive stop

blocks/mechanism to prevent inward swing without

fail.  Will not interfere with loading maximum size,

packages or load/unload tray in stow position

(approx. 1 inch gap).

Enclosure (2) Sheet 6 of 11

| 27 | Dedicated Communication system |  | No missing or defective call-signal stations, head/chest or hand sets. Each call signal station is located adjacent to each control station. |
| --- | --- | --- | --- |
| 28 | CONTROLS Motor controller: |  | No moisture, corrosion, or loose, missing, broken, frayed or burnt electrical or mechanical connections/components/contacts on any motor controller components apparent by visual and hands on inspection. All wiring is properly sized for load requirements apparent by comparing motor nameplate voltage/current data to wire ratings. No missing, broken, disconnected or non-operational 5-ampere control circuit fuses or fuse holders. |
|  | Up/down relays |  | The up/down electromechanical relay mechanical interlock is installed and properly aligned, and armatures operate smoothly with no evidence of binding or sticking apparent by hands-on test and inspection. |
|  | Power on/off switch |  | The motor controller power on/off switch is properly installed and labeled on the outside of the door and operational apparent by SOT and visual inspection. |
|  | Status/fault indicators |  | The motor controller indicator panel located on the outside of the motor controller door has no missing, broken, disconnected or non-operational status or fault indicator sockets or bulbs apparent by hands-on inspection and BITE panel lamp test push-button test. |
|  | BITE panel |  | The BITE panel located on the inside of the motor controller door has no missing, broken, disconnected or non-operational 1 ampere fuses or fuse holders. No missing, broken, disconnected or non-operational status or fault indicator sockets or bulbs. Is operational apparent by SOT and visual inspection. |
|  | Time relays |  | The timing relays are operational and properly adjusted to provide the required delay period (timing on and/or timing off) apparent by SOT and hands-on inspection. Refer to Tech Manuel for adjustment Procedures. |
|  | Current protection |  | The thermal overload relay heater coils are sized IAW motor nameplate data, properly installed and set to 100% apparent by visual hands-on inspection. The instantaneous overload relay current setting is set to 110% of actual rated load current draw (taken in the up direction) apparent by the conveyor technical manual corrective maintenance adjustment procedure |
|  | In-trunk control and safety switches: |  | Not missing, damaged, or misaligned, and are correctly oriented and securely fastened (see note). Conveyor down continuous operation shall stop when the down overtravel, down interlock or jam limit switch(es) is/are actuated. Conveyor up continuous operation shall stop when either the up overtravel, or jam limit switch(es) is/are actuated. |
|  | Down overtravel |  | Down overtravel switch will stop and prevent all conveyor downward movement when actuated without fail. Will allow upward movement to clear package. Switch arm roller will be adjusted to within 1/32 of an inch to actuator apparent by visual and hands-on inspection/measurement. |
|  | Down interlock |  | Down interlock switch will stop and prevent all conveyor downward movement when actuated without fail. Will allow upward movement to pickup packages during strike-up operations. Will be installed with all adjustable load/unload trays that intermesh with carrier trays (intermediate and bottom level load stations), and be actuated when placed in the load (horizontal) position. |
|  | Index proximity |  | Index proximity switch will be installed to stop every carrier tray at the index level load/unload device: height, +2 inches/-0 inches when flagged by a passing carrier tray. Will initiate 1K12 (index timing relay) to prevent restarting up operation for approx. 4 seconds. |
|  | Jam limit |  | Jam limit switch or photoelectric device (DD 963 Class only) will stop and prevent all conveyor operation when actuated without fail. Switch arm roller will be adjusted to within 1/32 of an inch to actuator (counter weight) apparent by visual and hands-on inspection/measurement. |
|  | Cleanout door |  | Cleanout door switch will stop and prevent all conveyor operation when released by opening the door without fail. |
|  | Hatch/Door interlock |  | Hatch/door (load station access hatch/doors only) interlock switch(es) will allow conveyor operation when released by any combination of 2 (two) open doors, and only 2 (two) open doors without fail. Switches are located away from door hinge side, and actuated by a door-mounted striker. |
|  | Up overtravel |  | Up overtravel photoelectric device will stop and prevent all conveyor movement, with top door closed, when actuated, by a stray package and not the times of a tray, without fail. |
|  | Stow Switch |  | Stow switch will stop and prevent all conveyor operation when a load station access door is closed and the load/unload tray is not in the stow position without fail. Will be installed in lieu of door blocks at load/unload station with adjustable load/unload trays that intermesh with carrier trays (index, intermediate and bottom level load stations), and are actuated by load/unload trays when placed in the stow (vertical) position. |
|  | Control Station |  | Not missing, damaged, or misaligned, are correctly orientated, assembled, watertight at a minimum or explosion proof (as required) and securely fastened. Are located to provide the supervisor clear vision of and access to the conveyor hatch/door opening to perform his duties as operator and/or handler while maintaining positive control of conveyor movement. All controls stations will provide up, down, index/continuous (index level only), and run/stop control switches, and lockable covers. |
|  | Lockable covers |  | Lockable covers, in the open or locked positions, shall not obstruct access to the run/stop switch. Shall, in the locked position, prevent access to the up/down push buttons and index/continuous switch. Shall be in the locked position and located at all times when not in use. |
|  | Up push-button |  | Up push button is a momentary contact type, properly labeled, the top component on the control station, and will start any upward operation when momentarily pushed-in at any level. |
|  | Down push-button |  | Down push button shall be a momentary contact type, properly labeled, the 2nd component down from the top on the control station, and will start downward operation when momentarily pushed in at any level. |
|  | Run/stop push/pull switch |  | Run/stop switch shall be a push/pull detented contact type with a red mushroom head, properly labeled, the bottom element of the control station, and will be interlocked to stop and prevent conveyor operation when in the stop (pushed-in) position at any control station. |
|  | Index/continuous switch (index level only) |  | Index/continuous switch shall be a rotary, detented contact, type switch, properly labeled, the third element of the index level (5 element) control station, and protected by the lockable cover when in the locked position. |
| 31 | Hand held remote emergency stop switch/stowage bracket: |  | Not damaged, is properly assembled, labeled, and watertight at a minimum or explosion proof (as required). |
|  | Emergency stop switch |  | Switch shall be a push/pull detented contact type with a red mushroom head, properly labeled, remotely located to provide the safety observer clear view of the trunk opening, handler(s) and supervisor during operation. Switch shall be interlocked to stop and prevent conveyor operations when in the stop (pushed-in) position at any level without fail. It will be connected using a 3 (three) conductor cable with 1 (one) conductor providing electric shock protection by electrically grounding the switch housing to ships hull. |
|  | Stowage bracket |  | Stowage bracket is remotely located in a convenient location that will not allow the emergency stop switch cable to cause a trip hazard to handler(s) or supervisor when deployed by the safety observer during operation. Stowage bracket is located 6 (six) to 10 (ten) feet from the control station and provides a holder for the approximately 10 (ten) foot of cable coil for the emergency stop switch. |
|  | Safety/warning placards: |  | Not damaged, are properly fabricated, sized, located, and securely fastened. |
|  | Operation instruction chart |  | Operating instruction chart shall be located adjacent to each control station in clear view of the supervisor during operation, and include specific operating instructions/modes of operation for that conveyor. |
|  | Two-Man Rule |  | Two-man rule shall be located directly to the inside of each conveyor door in clear view of the supervisor and handlers during operation. |
|  | Warnings |  | Warning plates shall be located either directly to each personnel safety shield (where installed) or the inside of each conveyor door, or the front of the rear trunk shield/guard in clear view of the supervisor and handler(s) before and during operation. |

CONVEYOR COMPONENT LOAD TEST REQUIREMENT

| COMPONENT | SUB-COMPONENT | VISUAL | NO LOAD | STATIC | DYNAMIC | RATED |
| --- | --- | --- | --- | --- | --- | --- |
|  | OR CONDITION |  |  | LOAD | LOAD | LOAD |
| Motor | New, repaired | X2 | X |  | X | X |
|  | Replace or tighten foundation hardware | X2 | X |  | X |  |
| Torque Limiter Coupling | New, repaired or after a jam or slippage noted | X | X |  | X |  |
|  | Replace key, tighten fasteners/hardware | X2 | X |  | X | X |
| Reduction Gear | New/repaired | X2 | X | X | X | X |
| Brake | Reinstalling brake, replacement of any load holding component | X2 | X | X | X |  |
|  | Disassembly of load holding portion of brake for inspection; adjustments No New Components | X | X |  |  | X |
| Jack Shaft | Repair/replacement | X2 | X |  | X |  |
| Pillow Block | Repair/replacement | X | X |  |  |  |
| Connecting Couplings | New/repaired, key replacement | X2 | X |  | X |  |
|  | Set screw replacement/tighten | X2 | X |  |  |  |
| Sprockets | New key, key way repair | X2 | X |  | X |  |
|  | Key realignment | X2 | X |  |  |  |
|  | Set screw/fastener/hardware replacement/tighten, bearing replacement | X | X |  |  | X |
| Drive/Driven Chains | New, remove or add link | X2 | X |  | X |  |
|  | Replacement/tighten fasteners, tensioning | X2 | X |  |  |  |
| Head Cam Assembly | Disassembly for repair or replacement of any component | X2 | X |  | X | X |
|  | Replacement or tightening of fasteners/hardware | X2 | X |  |  |  |
| Carrier Chain | New | X2 | X | X | X | X |
|  | Repair or replace link, pins | X2 | X |  | X |  |
|  | Replace/tighten fasteners, tensioning | X2 | X |  |  | X |
| Guide Arm Assembly | New assembly, reinstalling assembly, shaft or block replacement/repair | S2 | X | X1 |  |  |
|  | Replacement of cam followers (rollers), spacers or fasteners/hardware | X | X |  |  | X1 |
| Cam Tracks | New/repaired | X | X |  |  |  |
| Tail Cam Assembly | Disassembly for repair or replacement of any component | X2 | X |  | X |  |
|  | Replacement or tightening of fasteners/hardware | X2 | X |  |  |  |
| Carrier Tray | New, repair or reinstalling | X2 | X | X1 |  |  |
|  | Replacement or tightening of fasteners/hardware | X2 | X |  |  |  |
| Load/Unloader | New, repair or reinstalling | X2 | X1 | X1 |  |  |
|  | Replacement or tightening of fasteners/hardware | X2 | X |  |  |  |
| Down Overtravel Device | New, repair, reinstalling replacement or tightening of components/fasteners/ hardware | X2 |  |  |  | X1 (15 pounds) |

LEGEND

X   - REQUIRED TEST

X1 - REQUIRED TEST FOR THAT ASSEMBLY BEING WORKED ON ONLY

X2 - PERFORM BEFORE AND AFTER LOAD TEST