# PROCESSING IN STEAM IN STILL RETORTS

| INSTRUCTIONS COMPLETE THE QUESTION BLOCKS BELOW. EACH BLOCK IS EXPANDABLE TO ACCOMMODATE NARRATION AS NEEDED. DRAW A DIAGRAM OF THE RETORT OR OBTAIN ONE FROM THE FIRM. ATTACH THE DIAGRAM TO THIS SURVEY REPORT. REPORT ALL PIPE SIZES AS INSIDE DIAMETER (ID). CROSS-SECTIONAL AREA = 3.14R² (R = ½ DIAMETER). MAKE A HARD COPY OF THE COMPLETED FORM AND ATTACH TO THE LACF INSPECTION REPORT. |
| --- |
| RETORT DESCRIPTION |
| RETORT NO. | TYPE OF RETORT: VERTICAL [] HORIZONTAL [] VERTICAL (CRATELESS) [] | LENGTH OR HEIGHT | DIAMETER |
| FOR VERTICAL RETORTS, BOTTOM CRATE SUPPORTS ARE PRESENT. YES [] NO [] |
| ARE BAFFLE PLATES PRESENT IN THE BOTTOM OF RETORT? YES [] NO [] |
| ARE THERE ANY PROTRUSIONS INSIDE THE RETORT OR THE RETORT DOOR CASING WHICH COULD DAMAGE CONTAINERS DURING LOADING/UNLOADING OF CRATES? YES [] NO [] |
| COMPUTER CONTROLS |
| DOES A COMPUTER CONTROL ANY OF THE RETORT FUNCTIONS? YES [] NO [] |
| DOES THE FIRM HAVE DOCUMENTATION ON HAND THAT INDICATES THAT THE COMPUTER SYSTEM HAS BEEN VALIDATED? YES [] NO [] EXPLAIN: |
| IS RECORD KEEPING PART OF THE COMPUTER FUNCTION? YES [] NO [] IF YES, DOES THE RECORD KEEPING COMPLY WITH 21CFR PART 11 YES [] NO [] |
| MERCURY THERMOMETERS (113.40(a)(1)) |
| IS THE RETORT EQUIPPED WITH A MIG THERMOMETER? YES [] NO [] |
| IS THE RETORT EQUIPPED WITH ANOTHER TYPE OF TEMPERATURE INDICATOR DEVICE? YES [] NO [] IF SO, DESCRIBE THE INDICATOR. |
| ARE SCALE DIVISIONS EASILY READABLE TO 1°F (.5°C)? YES [] NO [] |
| NO. OF DEGREES F OR C/IN. OF GRADUATED SCALE: ____________. (TEMP. RANGE MUST NOT EXCEED 17°F(8°C) PER INCH (4°/CM) OF GRADUATED SCALE – 113.40(a)(1) (ALSO, SEE LACF GUIDE, P. 14) | DATE LAST TESTED FOR ACCURACY |
| THERMOMETERS SHALL BE TESTED FOR ACCURACY AGAINST A KNOWN ACCURATE STANDARD THERMOMETER UPON INSTALLATION AND AT LEAST ONCE A YEAR THEREAFTER; RECORDS OF ACCURACY CHECKS THAT SPECIFY DATE, STANDARD USED, METHOD USED, AND PERSON PERFORMING THE TEST SHOULD BE MAINTAINED. EACH THERMOMETER SHOULD HAVE A TAG, SEAL, OR OTHER MEANS OF IDENTITY THAT INCLUDES THE DATE IT WAS LAST TESTED FOR ACCURACY – 113.40(a)(1). |
| STANDARD USED FOR THE TEST: |
| NAME AND TITLE OF PERSON WHO PERFORMED TEST: |
| IS THE LAST TEST DATE IDENTIFIED ON THE THERMOMETER? YES [] NO[] |
| DESCRIBE THE FIRM’S ACTIONS REGARDING MIG THERMOMETERS THAT WERE OUT OF CALIBRATION. |
| IS THE MERCURY UNDIVIDED? YES [] NO [] (A THERMOMETER THAT HAS A DIVIDED MERCURY COLUMN OR THAT CANNOT BE ADJUSTED TO THE STANDARD SHALL BE REPAIRED OR REPLACED, 113.40(A)(1)) |
| WHEN MIG THERMOMETERS ARE FOUND TO BE PROVIDING READINGS ABOVE THE ACTUAL TEMPERATURES, DOES THE FIRM EVALUATE PRODUCTS PRODUCED USING THOSE THERMOMETERS? YES [] NO [] DESCRIBE THE FIRM’S PROCEDURES. |
| IS THE THERMOMETER LOCATED WHERE IT IS EASY TO READ ACCURATELY? YES [] NO [] SHALL REQUIREMENT– 113.40(a)(1) |
| THE SENSOR BULB IS LOCATED IN THE RETORT SHELL [], OR EXTERNAL WELL [] |
| DIAMETER OF OPENING TO EXTERNAL WELL:_______ (DIA. MUST BE AT LEAST 3/4-IN. 113.40(a)(1) | BLEEDER SIZE: ______________ (1/16-IN. MINIMUM – 113.40(a)(1) |
| DOES THE BLEEDER EMIT STEAM CONTINUOUSLY DURING PROCESSING? YES [] NO [] IF NO, EXPLAIN. (SHALL REQUIREMENT – 113.40(a)(1)) |
| IF A MUFFLER IS USED ON BLEEDER(S), WHAT EVIDENCE DOES THE FIRM HAVE THAT IT DOES NOT RESTRICT FREE FLOW OF STEAM? (113.87(g) |
| IS THE MERCURY THERMOMETER USED AS THE REFERENCED INSTRUMENT DURING PROCESSING? YES [] NO [] (SHALL REQUIREMENT – 113.40(a)(1)) |
| TEMPERATURE RECORDER |
| TYPE OF TEMPERATURE RECORDER: ROUND CIRCULAR CHART [] STRIP CHART [] OTHER [] IF OTHER, DESCRIBE. |
| DO THE CHART SPECIFICATIONS MEET THE REQUIREMENTS OF PART 113? YES [] NO[] (GRADUATIONS ON THE TEMPERATURE-RECORDING DEVICE SHALL NOT EXCEED 2°F (1°C) WITHIN A RANGE OF 10°F (5.5°C) OF THE PROCESSING TEMPERATURE. EACH CHART SHALL HAVE A WORKING SCALE OF NOT MORE THAN 55°F/IN (12°C/CM) WITHIN A RANGE OF 20°F (10°C) OF THE PROCESSING TEMPERATURE – 113.40(b)(2)). ALSO, SEE P. 14 OF LACF FIELD GUIDE-PART 2. |
| IS THE TEMPERATURE CHART ADJUSTED TO AGREE AS NEARLY AS POSSIBLE WITH BUT NOT HIGHER THAN THE KNOWN ACCURATE MERCURY-IN-GLASS THERMOMETER DURING THE PROCESSING PERIOD? YES [] NO [] SHALL REQUIREMENT - 113.40(B)(2). NOTE ANY DIFFERENCE BETWEEN THE RECORDING THERMOMETER AND THE MERCURY-IN-GLASS THERMOMETER AND WHICH READING IS HIGHER. |
| IS THERE A MEANS FOR PREVENTING UNAUTHORIZED ADJUSTMENTS? YES [] NO [] (A MEANS OF PREVENTING UNAUTHORIZED CHANGES IN ADJUSTMENTS SHALL BE PROVIDED. A LOCK OR NOTICE FROM MANAGEMENT STATING “ONLY AUTHORIZED PERSONS ARE PERMITTED TO MAKE ADJUSTMENTS” & POSTED AT OR NEAR THE RECORDING DEVICE IS A SATISFACTORY MEANS FOR PREVENTING UNAUTHORIZED CHANGES. 113.40(B)(2)) |
| IS THE CHART DRIVE TIMING MECHANISM ACCURATE? YES [] NO [] IF NO, EXPLAIN. |
| IS THE RECORDER COMBINED WITH A STEAM CONTROLLER? YES [] NO [] |
| THE TEMPERATURE SENSING BULB IS INSTALLED IN THE RETORT SHELL [], EXTERNAL WELL []. (THE TEMPERATURE-RECORDER BULB SHALL BE INSTALLED EITHER WITHIN THE RETORT SHELL OR IN A WELL ATTACHED TO THE SHELL - 113.40(b)(2)). |
| DOES THE TEMPERATURE RECORDER BULB WELL HAVE A 1/16-IN. DIA. OR LARGER BLEEDER THAT EMITS STEAM CONTINUOUSLY DURING THE PROCESSING PERIOD? YES [] NO [] N/A [] SHALL REQUIREMENT – 113.40(b)(2) |
| IF A MUFFLER IS USED ON THE BLEEDER, WHAT EVIDENCE DOES THE FIRM HAVE THAT IT DOES NOT RESTRICT THE FLOW OF STEAM? 113.87(g) |
| PRESSURE GAGE |
| IF A PRESSURE GAGE IS PRESENT, IS IT GRADUATED IN DIVISIONS OF 2 LBS. OR LESS? YES [] NO [] NOTE – THIS IS A RECOMMENDATION - “SHOULD” REQUIREMENT OF THE REGULATIONS. |
| AUTOMATIC STEAM CONTROLLER |
| IS THE STEAM CONTROLLER AUTOMATIC? YES [] NO [] EACH RETORT SHALL BE EQUIPPED WITH AN AUTOMATIC STEAM CONTROLLER TO MAINTAIN THE RETORT TEMPERATURE 113.40(a)(4). |
| IS THE STEAM CONTROLLER TEMPERATURE OR PRESSURE ACTUATED? TEMP [] PRESS [] (THE STEAM CONTROLLER MAY BE ACTUATED BY A TEMPERATURE SENSOR POSITIONED NEAR THE MERCURY-IN-GLASS THERMOMETER; A STEAM CONTROLLER ACTIVATED BY THE STEAM PRESSURE OF THE RETORT IS ACCEPTABLE IF IT IS CAREFULLY MAINTAINED SO IT OPERATES SATISFACTORILY 113.40(a)(4)). |
| REPORT THE MANUFACTURER, MODEL, TYPE AND SIZE OF THE AUTOMATIC STEAM CONTROL VALVE? |
| IF THE TEMPERATURE (STEAM) CONTROLLER IS AIR OPERATED, DOES THE SYSTEM HAVE AN ADEQUATE FILTER TO ASSURE A SUPPLY OF CLEAN, DRY AIR? YES [] NO [] AIR OPERATED TEMPERATURE CONTROLLERS SHOULD HAVE ADEQUATE FILTER SYSTEMS TO ASSURE A SUPPLY OF CLEAN, DRY AIR 113.40(A)(2). |
| STEAM INLETS |
| ARE STEAM INLETS LOCATED OPPOSITE THE VENT? YES [] NO [] IF NO, EXPLAIN. (THE VENT SHALL BE LOCATED OPPOSITE THE STEAM INLET – 113.40(A)(12)) |
| INSIDE DIAMETER(S) OF SMALLEST RESTRICTION(S)IN THE STEAM INLET LINES (INCLUDE THE TEMPERATURE (STEAM) CONTROL VALVE AS A RESTRICTION): |
| CALCULATED CROSS SECTIONAL AREA(S) OF SMALLEST RESTRICTIONS = _____________ A = 3.14(R)² |
| STEAM SPREADER |
| DESCRIBE SHAPE AND DIMENSIONS: (NOTE – STEAM SPREADERS ARE REQUIRED FOR HORIZONTAL RETORTS. VERTICAL RETORTS ARE NOT REQUIRED TO HAVE STEAM SPREADERS. HOWEVER, IF THEY HAVE THEM, THEY MUST BE MAINTAINED – SEE P. 24 OF LACF FIELD GUIDE-PART 2) |
| IF THE RETORT IS OVER 30 FT. LONG, ARE THERE 2 STEAM INLETS? YES [] NO [] IF NO, HOW MANY? (113.40(a)(7)) (SHOULD REQUIREMENT) |
| NUMBER OF PERFORATIONS: | DIAMETER OF PERFORATIONS: |
| ARE PERFORATIONS CLEARLY OPEN? YES [] NO [] IF NO, EXPLAIN. |
| IS THE STEAM SPREADER IN GOOD REPAIR? (E.G. HOLES HAVE NOT BEEN ENLARGED BY WEAR; PIPES HAVE NOT RUSTED THROUGH) YES [] NO [] |
| THE CALCULATED TOTAL CROSS-SECTIONAL AREA OF THE PERFORATIONS: (NO. OF PERFORATIONS) X (3.14) X (R²) |
| IS THIS AREA 1.5 TO 2 TIMES THE TOTAL CROSS SECTIONAL AREA(S) OF THE SMALLEST RESTRICTIONS(S) IN THE STEAM INLET LINE? YES [] NO [] (THE NUMBER OF PERFORATIONS SHOULD BE SUCH THAT THE TOTAL CROSS-SECTIONAL AREA OF THE PERFORATIONS IS EQUAL TO 1.5 TO 2 TIMES THE CROSS-SECTIONAL AREA OF THE SMALLEST RESTRICTION IN THE STEAM INLET LINE) 113.40(a)(7)) |
| BLEEDERS (113.40(a)(8) |
| NUMBER OF BLEEDERS: | SIZE(S) | LOCATION (INCLUDE DISTANCE BETWEEN BLEEDERS ON HORIZONTAL RETORTS): |
| ARE THEY OBSERVABLE DURING OPERATION? YES [] NO [] |
| ARE THEY WIDE OPEN DURING THE ENTIRE PROCESS INCLUDING THE COME-UP TIME? YES [] NO [] IF NO, EXPLAIN. |
| IF A MUFFLER IS USED OVER THE BLEEDERS, WHAT EVIDENCE DOES THE FIRM HAVE THAT IT DOES NOT RESTRICT FREE FLOW OF STEAM? 113.87(g) |
| BLEEDERS ON CRATELESS RETORTS |
| IN RETORTS HAVING TOP STEAM INLET AND BOTTOM VENTING, A BLEEDER SHALL BE INSTALLED IN THE BOTTOM TO REMOVE CONDENSATE – 113.40(a)(8). IT IS RECOMMENDED THAT THERE BE 1 OR MORE 3/8-INCH OR LARGER CONDENSATE BLEEDERS AT THE BOTTOM OF THE RETORT. IN ADDITION, WHEN A FALSE BOTTOM IS EMPLOYED, IT IS USEFUL TO HAVE A 1/8-INCH BLEEDER WITH ITS OPENING AT A POINT HIGHER THAN THE CONDENSATE BLEEDER AND JUST BELOW THE FALSE BOTTOM (SEE NFPA BUL 26-L, 13TH EDITION, P. 14 AND LACF FIELD GUIDE-PART 2, P. 26). IN SOME SYSTEMS, A CONDENSATE TRAP MAY BE USED TO COLLECT CONDENSATE BUILDUP AT THE BOTTOM OF THE RETORT IN LIEU OF A STEAM CONDENSATE BLEEDER – IN THIS CASE, THE REMOVAL OF CONDENSATE MAY NOT BE VISIBLE, HOWEVER, A VISIBLE STEAM BLEEDER SHOULD BE LOCATED ABOVE THE CONDENSATE TRAP (JUST BELOW THE FALSE BOTTOM). THIS STEAM BLEEDER SHOULD EMIT ONLY STEAM AND NO CONDENSATE OR WATER DURING THERMAL PROCESSING. |
| IS THE RETORT EQUIPPED WITH A FALSE BOTTOM TO PREVENT CONTAINERS FROM CONTACTING CONDENSATE? YES [] NO [] IF SO, IS CONDENSATE REMOVED BY A CONDENSATE BLEEDER(S) [] OR A STEAM TRAP []? IS THE CONDENSATE BLEEDER(S)/TRAP CONNECTED AT THE BOTTOM OF THE RETORT? YES [] NO [] N/A [] IS IT VISIBLE TO THE RETORT OPERATOR? YES [] NO [] N/A [] WHAT IS THE DIAMETER OF THE STEAM CONDENSATE BLEEDER? ________. IF A STEAM TRAP IS USED, WHERE IS IT POSITIONED? |
| IS THE RETORT EQUIPPED WITH A STEAM BLEEDER(S) BETWEEN THE FALSE BOTTOM DOOR AND THE BOTTOM OF THE RETORT? YES [] NO [] IF SO, REPORT THE NUMBER AND DIAMETER OF THE BLEEDER(S): |
| DOES THE OPERATOR OBSERVE A FREE FLOW OF STEAM FROM THIS BLEEDER PRIOR TO BEGINNING THE RETORT THERMAL PROCESS TIMING AND AT INTERVALS OF SUFFICIENT FREQUENCY DURING THE PROCESS? YES [] NO [] ARE THESE OBSERVATIONS RECORDED AT THE TIME THEY ARE MADE? YES [] NO []. |
| IF A STEAM CONDENSATE BLEEDER(S) IS PRESENT, DOES THE OPERATOR ALSO OBSERVE THE FREE FLOW OF STEAM CONDENSATE FROM THIS BLEEDER JUST BEFORE AND DURING THE THERMAL PROCESS? YES [] NO [] ARE THESE OBSERVATIONS RECORDED AT THE TIME THEY ARE MADE? YES [] NO []. |
| AIR OR WATER COOLING LINE VALVES |
| IS WATER OR COMPRESSED AIR USED DURING COOLING? WATER [] AIR [] |
| TYPE OF VALVE ON WATER COOLING LINES SUPPLYING RETORT: WERE WATER LINES OBSERVED TO BE LEAKING? YES [] NO [] |
| TYPE OF VALVE ON THE AIR SUPPLY LINE TO THE RETORT. WERE AIR LINES OBSERVED TO BE LEAKING? YES [] NO [] |
| VENTS |
| NUMBER OF VENTS: | SIZE(S) – DIAMETER [ ] LENGTH [ ] |
| WHAT IS THE VALVE TYPE? GATE [] PLUG COCK [] OTHER [] (SPECIFY) |
| ARE VENTS FULLY OPEN DURING VENTING? YES [] NO [] IF NO, EXPLAIN |
| IS A STEAM BY-PASS VALVE USED DURING VENTING? YES [] NO [] IF YES, EXPLAIN. (NOTE – VENTING PROCEDURES AND ARRANGEMENTS MUST BE THE SAME AS USED DURING THE TEMPERATURE DISTRIBUTION STUDY THAT WAS CONDUCTED ON THE RETORT TO ESTABLISH THE VENT SCHEDULE) |
| ARE VENTS LOCATED OPPOSITE THE STEAM INLET? YES [] NO [] IF NO, EXPLAIN. (VENTS SHALL BE LOCATED OPPOSITE STEAM INLET – 113.40(A)(12)) |
| IF VENTS ARE CONNECTED TO A RETORT MANIFOLD, WHAT IS THE MANIFOLD VALVE TYPE? GATE [] PLUG COCK [] OTHER [] (SPECIFY) (WHERE A RETORT MANIFOLD CONNECTS SEVERAL VENT PIPES FROM A SINGLE RETORT, IT SHALL BE CONTROLLED BY A GATE, PLUG COCK OR OTHER ADEQUATE TYPE VALVE 113.40(a)(12). |
| RETORT MANIFOLD DIAMETER AND CROSS-SECTIONAL AREA: DIA. = _____. A = _____. (CROSS SEC. AREA = (3.14) X (R²)) |
| NUMBER OF VENTS CONNECTING TO MANIFOLD: | DIAMETER OF CONNECTING VENTS: |
| THE CROSS-SECTIONAL AREA OF ALL CONNECTING VENTS:_________. A = (NO. VENTS)X(3.14)X(R²) |
| IS THIS LARGER THAN THE CROSS-SECTIONAL AREA OF THE RETORT MANIFOLD? YES [] NO [] (THE RETORT MANIFOLD SHALL BE OF A SIZE THAT THE CROSS-SECTIONAL AREA OF THE PIPE IS LARGER THAN THE TOTAL CROSS-SECTIONAL AREA OF ALL CONNECTING VENTS 113.40(a)(12)) |
| DOES THE VENT, RETORT MANIFOLD OR MANIFOLD HEADER BREAK TO THE ATMOSPHERE? YES [] NO [] IF YES, WHERE? IF NO, EXPLAIN. (A MANIFOLD HEADER CONNECTING VENTS OR MANIFOLDS FROM SEVERAL STILL RETORTS SHALL LEAD TO THE ATMOSPHERE – 113.40(a) (12)) |
| DIAMETER AND CROSS-SECTIONAL AREA OF MANIFOLD HEADER (IF APPLICABLE): DIAMETER = __________; A = ___________. |
| DIAMETERS AND TOTAL CROSS-SECTIONAL AREA OF CONNECTING VENTS/MANIFOLDS FROM ALL RETORTS VENTING SIMULTANEOUSLY: DAI. = _____________; A = ________. A = (NO. OF CONNECTING MANIFOLDS)X(3.14)X(R²) |
| IS THE MANIFOLD HEADER CROSS-SECTIONAL AREA AT LEAST EQUAL TO THIS AREA? YES [] NO [] (THE MANIFOLD HEADER SHALL BE OF A SIZE THAT THE CROSS-SECTIONAL AREA IS AT LEAST EQUAL TO THE TOTAL CROSS-SECTIONAL AREA OF ALL CONNECTING RETORT MANIFOLD PIPES FROM ALL RETORTS VENTING SIMULTANEOUSLY – 113.40(a)(12)) |
| IS THERE A VALVE ON THE MANIFOLD HEADER? YES [] NO [] (THE MANIFOLD HEADER SHALL NOT BE CONTROLLED BY A VALVE – 113.40(a)(12)) |
| DO VENTING ARRANGEMENTS AND METHODS COMPLY WITH ONE OF THE EXAMPLES IN 113.40(A)(12)? YES [] NO [] IF NO, DOES THE FIRM HAVE HEAT DISTRIBUTION DATA OR SUITABLE DOCUMENTATION THAT APPROPRIATE TESTS HAVE BEEN PERFORMED? YES [] NO [] 113.40(a)(12)(III). |
| IF VENTS ARE EQUIPPED WITH MUFFLERS,SPECIFY TYPE AND PERFORMANCE CHARACTERISTICS. WHAT EVIDENCE DOES THE FIRM HAVE THAT THE MUFFLER ALLOWS ADEQUATE VENTING (SEE 113.87(g)? |
| DIVIDER PLATES AND RETORT BASKET - 113.40(a)(9) |
| DIVIDER PLATES ARE USED? YES [] NO [] |
| THE PLATES ARE UNIFORMLY PERFORATED? YES [] NO [] |
| THE PERFORATIONS ARE AT LEAST 1-IN. HOLES ON 2-IN CENTERS OR THE EQUIVALENT? YES [] NO [] (PROVIDE HOLE SIZE AND DISTRIBUTION (E.G. ¼” ON ½” CENTERS) |
| ARE RETORT BASKETS UNIFORMLY PERFORATED? YES [] NO [] DESCRIBE. |
| DO BASKET BOTTOMS HAVE AT LEAST 1-IN. HOLES ON 2-IN. CENTERS OR THE EQUIVALENT? YES [] NO [] |
| DOES FIRM HAVE DOCUMENTATION ON FILE THAT PERMITS VENTING USING DIVIDER PLATES AND THE CURRENT BASKET DESIGN? YES [] NO |